## Slide 1
MATRIX MULTIPLIER
VHDL IMPLEMENTATION
Megan Maremmani
Eleni Zewdu Belayhun
Master Of Science in Computer Engineering
Electronics and Communications Systems

## Slide 2
PROBLEM DESCRIPTION
THE DESIGN:
Matrix Multiplication is a very useful and fundamental operation in various scientific fields
The request is to design a digital circuit that implements a matrix multiplication

## Slide 3
PORTS DESCRIPTION
INPUTS:
OUTPUTS:
To improve code readability and modularity, a dedicated signals package is included to reference the system’s inputs and outputs in a clean and structured manner
clk : Clock signal
rst : Reset signal (active high)
N_size : Rows for A and C
M_size : Columns for A and rows for B
K_size : Columns for Matrices B and C
A_row : In A stored row-wise
B_column : In B stored column-wise
A_valid : Valid signal for A
B_valid : Valid signal for B
C_row : Output matrix C stored row-wise
C_valid : Output valid signal for C

## Slide 4
BLOCK DIAGRAM
Circuit’s block diagram

## Slide 5
LOOK UP TABLES (LUT)
Matrix_LUT_A:
Matrix_LUT_B:
An implementation of LUTs has been made:
Stores input data for Matrix A in a row-wise format.
Data is loaded sequentially and fully before computation begins to ensure synchronization with the system and the second LUT.
Stores input data for Matrix B in a column-wise format.
Data is loaded sequentially and fully before computation begins to ensure synchronization with the system and the second LUT.

## Slide 6
MULTIPLIER AND LUT_C
Matrix_LUT_C: Stores results of the multiplication in row-wise format.
Each element is written to its corresponding address and mapped to C_row, with C_valid indicating result validity.
MatrixMultiplier
Implemented using a Finite State Machine (FSM)
Processes:
state_reg: synchronous state transitions and counter updates based on clock/reset.
FSM: Defines next states and control signals.
MUL: Performs dot product operations during multiplication phase.
RESULT_OUT: Assembles and outputs Matrix C row by row, signaling readiness via C_valid.

## Slide 7
MULTIPLIER 2/2
STATES DEFINITION
IDLE: Initial state; system is ready and initialized.
LOAD_MAT: Loads data into LUTs and synchronizes inputs.
CHECK: Ensures all preconditions for multiplication are met.
MULTIPLY: Performs matrix multiplication.
MAT_C: Stores multiplication results into output
LUT_RESULT: Prepares final matrix C for output, row by row.
END_MUL: Indicates completion of the multiplication process
MatrixMultiplier

## Slide 8
TEST BENCH – TEST PLAN
Loading of one LUT with values
The matrix multiplication was verified using a VHDL testbench in ModelSim-Intel FPGA Standard Edition.
A 3×3 matrix configuration was chosen to balance simplicity and thoroughness.
Testbench validates functional correctness based on input dimensions.
Simulation progress and key events are tracked through reports.

## Slide 9
SOME HIGHLIGHTS
LUT C result storage

## Slide 10
SOME HIGHLIGHTS
output of the results

## Slide 11
SYNTHESIS
The synthesis was done without mapping the actual physical I/O ports of the FPGA pins, using the -mode out_of_context option.
A warning came up during simulation:
because we used the out of context mode, so the accuracy of the timing is affected, however this does not impact the validity of the current results

## Slide 12
TIMING REPORT
The design timing summary confirms that all user-specified timing constraints for the matrix multiplier implementation have been successfully met

## Slide 13
MOST CRITICAL PATH
The timing analysis of the matrix multiplier design, highlights the most critical path. The most critical timing path is "Path 1", exhibiting the lowest slack value of 1.484 ns.

## Slide 14
POWER CONSUMPTION REPORT
Most of this power, approximately 95% (0.090 W), is attributed to static device power, which is inherent to the FPGA hardware itself regardless of activity.
The remaining 5% (0.004 W) corresponds to dynamic power, which is associated with the switching activity of the design during operation.
WHAT HAPPENS:

## Slide 15
RESOURCE UTILIZATION REPORT
The implementation utilizes only 236 Look-Up Tables (LUTs), resulting in a utilization rate of just 1.34%.
Similarly, it consumes 249 Flip-Flops (FFs), corresponding to a minimal 0.71% utilization.

## Slide 16
CONCLUSION:
TO THE FUTURE!
We implemented a Matrix Multiplier in VHDL for FPGA use.
Integrated a wrapper module for register-logic-register architecture, enabling easier performance analysis.
Verified functionality with a 3×3 matrix using a VHDL testbench in ModelSim, providing a balance of simplicity and functionality.
Scalability: Expand design to support larger matrices and higher precision (e.g., increased word length).
Modularity: change matrix dimensions.
Optimization: Explore pipelining and parallelism for higher performance in real-time systems.
FUTURE:
OUR GOAL:

## Slide 17
THANKS FOR
THE ATTENTION
Megan Maremmani
Eleni Zewdu Belayhun
Master Of Science in Computer Engineering
Electronics and Communications Systems